## Slide 1
Last changes: November 30 2022
The PASAPAS procedure and the users procedures available on : http://www-cast3m.cea.fr/index.php?xml=formations
François DI PAOLA, Caroline GUERIN

## Slide 2: Summary
  Introduction to Cast3M and reminders on PASAPAS
  PASAPAS operation
  Finding the mechanical equilibrium: UNPAS
  Exercise 1: following load
  Exercise 2: failure by elements removal
  Finding the thermal equilibrium: TRANSNON
  Exercise 3: variable heat source
  Exercise 4: thermo-mechanical contact

## Slide 3: Introduction to Cast3M reminders on PASAPAS

## Slide 4: Cast3M, quid ?
A finite element software
for structural and fluid mechanics
  Partial differential equations solved with the finite element method
  Complete software: solver, pre-processing and post-processing, visualization
  Based on an objet-oriented programming language: Gibiane

## Slide 5: Modeling in Numerous AREAS
  Structural mechanics (historical field)
    Quasi-static (non linear materials, geometry, boundary conditions)
    Contact/friction, Buckling
    Dynamics (temporal, modal, fluid structure interaction)
    Fracture mechnics (XFEM, dynamic propagation, cohesive zone model)
  Thermal analysis
    Conduction, convection, radiation, phase transition
  Fluid mechanics
  Metallurgy
  Magnetostatics
  Multi spieces diffusion (Fick’s law)
  Thermo-hydro-mechanical coupling

## Slide 6: The PASAPAS Procedure
  Objective
    incremental solving of non linear progressive thermal and mechanical problems
    time can be physical (e.g. thermal transients) or not (e.g. plasticity with progressive loading)
     time or pseudo-time is called the evolution parameter
  Non linear phenomena considered
  behavior (plasticity, damage, variable material properties, …)
  geometry (large displacements)
  strains (large rotations)
  boundary conditions (radiation, friction, following pressure, …)

## Slide 7: PASAPAS use
  Create a table containing all the data:
    TAB1 = TABL ;
    TAB1 . MODELE = MOD1 ET MOD2 ;
    TAB1 . CARACTERISTIQUES = MAT1 ET MAT2 ;
    TAB1 . BLOCAGES_MECANIQUES = BLO1 ;
    TAB1 . CHARGEMENT = CHA1 ET CHA2 ET CHA3 ;
    TAB1 . TEMPS_CALCULES = PROG 0.1 'PAS' 0.1 50. ;
    TAB1 . TEMPS_SAUVES = PROG 4. 8. 15. 16. 23. 42. ;
    TAB1 . PRECISION = 1.E-6 ;
    TAB1 . GRANDS_DEPLACEMENTS = VRAI ;
    …
  Procedure call: PASAPAS TAB1 ;
  Results post-processing
some indexes are required
other are optional

## Slide 8: Overview of input parameters
  General
    MODELE (MMODEL) Equations to solve, F. E. formulation (MODE)
    CARACTERISTIQUES (MCHAML) Material and/or geometrical parameters (MATE)
    CHARGEMENT (CHARGEME) Boundary conditions and loading variation during calculation (CHAR)
  Thermal analysis
  BLOCAGES_THERMIQUES (RIGIDITE) Stiffness matrix associated to the imposed values of the unknowns (DIRICHLET boundary conditions) (BLOQ)
CELSIUS (LOGIQUE) =VRAI (true) if temperature unit is CELSIUS
TEMPERATURES . 0 (CHPOINT) Initial conditions
  Mechanics
  BLOCAGES_MECANIQUES (RIGIDITE) Stiffness matrix associated to the imposed values of the unknowns (DIRICHLET boundary conditions) (BLOQ)
GRANDS_DEPLACEMENTS (LOGIQUE) Equilibrium checked on the deformed mesh
  DEPLACEMENTS . 0 (CHPOINT)
  CONTRAINTES . 0 (MCHAML)
  VARIABLES_INTERNES . 0 (MCHAML)
  DEFORMATIONS_INELASTIQUES . 0 (MCHAML)
Initial conditions

## Slide 9: Overview of input parameters
  Mechanics (dynamics)
    DYNAMIQUE (LOGIQUE) =VRAI (true) for dynamics calculations
    AMORTISSEMENT (RIGIDITE) Damping matrix
    VITESSES . 0 (CHPOINT)
    ACCELERATIONS . 0 (CHPOINT)
  List of the values of evolution parameter
    TEMPS_CALCULES (LISTREEL) List of the values of the evolution parameter (or time) for which results are requested
TEMPS_SAUVES (LISTREEL) List of times for which results are saved
OPTI 'SAUV' 'my_file' ;
TEMPS_SAUVEGARDES (LISTREEL) List of times for which SAUV operator is called
MES_SAUVEGARDES (TABLE) Results to be stored in addition to those automatically stored (total strains, …)
Initial conditions

## Slide 10: Overview of output parameters
  Results are stored in the table
TEMPS (TABLE) Times values, corresponding to « TEMPS_SAUVES »
    TEMPERATURES (TABLE)
    PROPORTIONS_PHASE (TABLE)
    DEPLACEMENTS (TABLE)
    CONTRAINTES (TABLE)
    DEFORMATIONS_INELASTIQUES (TABLE)
    VARIABLES_INTERNES (TABLE)
    REACTIONS (TABLE)
    VITESSES (TABLE)
    ACCELERATIONS (TABLE)
Fields (solution) calculated for each stored time « TEMPS_SAUVES »

## Slide 11: Post processing (examples)
  Solution fields extraction:
  from the table index
  SIG1 = TAB1 . CONTRAINTES . 5 ;
  or from the calculation time
  SIG1 = PECHE TAB1 'CONTRAINTES' 28.3 ;
  Graphical mode, interactive plot (limited):
  EXPLORER TAB1 ;
  Evolution of calculated field with time:
  EV1 = EVOL 'TEMP' TAB1 'DEPLACEMENTS' 'UX' P1 ;

## Slide 12: PASAPAS operation

## Slide 13: PASAPAS operation
  Main algorithm
    Initializations
    Loop on time steps (BEXTERN)
    Loop for thermo-mechanical convergence (BO_BOTH)
    Thermal solving [for the step]
    Mechanical solving [for the step]
    Thermo-mechanical convergence?
    Results recording
    End
    + User procedures calls (optional, user have to ask it)
    PERSO1 PERSO2 REEV_MEC REEV_THE CHARMECA CHARTHER PARATHER
    procedures to be defined by the user!

## Slide 14: PASAPAS operation
Initializations, PERSO1, REEV_MEC, REEV_THE
Time step initialization
REEV_THE
Thermal solving
Mechanics solving
REEV_MEC
Next time step Initialization
PERSO1
Results storage
End
Convergence?
Time steps end?
no
no
yes
yes
Options reading, initializations (materials, unknowns, temporary variables, indicators…), calculation times WTABLE, …
Call of the procedure for thermal calculation: TRANSNON, TRANSLIN or DUPONT2
(in the case of large displacements, solving on the last deformed shape)
Results are stored in ESTIMATION
User procedure (if asked)
Call to the procedure for mechanical calculation UNPAS
Results are stored in ESTIMATION
User procedure (if asked)
Test of convergence for thermo-mechanics, to activate with:
TAB1 . CONVERGENCE_MEC_THE = VRAI ;
[MAXI ABS (Ti–Ti-1)] / [MAXI ABS Ti] < CRITERE_COHERENCE (10E-2)
User procedure (if asked)
PAS_RESU: writing in CONTINUATION quantities of ESTIMATION
PAS_SAUV: writing in TAB1 if the time step belongs to TEMPS_SAUVE,
call to SAUV if the time step belongs to TEMPS_SAUVEGARDE
Recording of the new state as the initial time step state in WTABLE
BEXTERN
BO_BOTH

## Slide 15: Access to PASAPAS data
  TAB1 . 'ESTIMATION' contains all results calculated/converged by TRANSNON and UNPAS but not converged for BO_BOTH loop
    TAB1 . 'ESTIMATION' . 'TEMPS'
    TAB1 . 'ESTIMATION' . 'DEPLACEMENTS'
    TAB1 . 'ESTIMATION' . 'CONTRAINTES'
    TAB1 . 'ESTIMATION' . 'TEMPERATURES'
    …
    …
  TAB1 . 'CONTINUATION' contains converged results (for BO_BOTH loop) this index is updated at the end of the time-step!!!  useful for PASAPAS restart
    TAB1 . 'CONTINUATION' . 'TEMPS'
    TAB1 . 'CONTINUATION' . 'DEPLACEMENTS'
    TAB1 . 'CONTINUATION' . 'CONTRAINTES'
    TAB1 . 'CONTINUATION' . 'TEMPERATURES'
    …
    …

## Slide 16: Access to PASAPAS data
  TAB1 . 'WTABLE'
  Contains all useful variables for PASAPAS (chosen options, models, materials and instant loading, intermediate results …)
  Some indexes:
    WTABLE . 'CHARGEMENT' Loading on the time step
    WTABLE . 'THER_COURANT' Value of temperature at last iteration (during a time step)
    WTABLE . 'BLOCAGES_MECANIQUES' Mechanical constraint matrix WTABLE . 'BLOCAGES_THERMIQUES' Thermal constraint matrix
    WTABLE . 'FOR' Configuration at the time step beginning WTABLE . 'FOR0' Initial Configuration
    WTABLE . 'MODELE' Models WTABLE . 'CARACTERISTIQUES' Material properties
    …
    For more information, see:
     Comments in procedure PAS_DEFA (http://www-cast3m.cea.fr/index.php?page=procedures&procedure=pas_defa)
     The PASAPAS documentation (http://www-cast3m.cea.fr/html/Documentation_Cast3M/Pasapas.pdf)

## Slide 17: Finding the mechanical equilibrium the UNPAS procedure

## Slide 18: Reminder on equations
  Local equations of the static equilibrium
    equilibrium on
    prescribed surface forces on
    prescribed displacements on
  Weak form + FE discretization
    Vectors of Equivalent nodal forces (N)
    to the prescribed surface forces (Pa) (PRES, FSUR, FORC, …)
    to the surface forces in reaction to the prescribed displacements (m) (REAC)
    to the prescribed volume forces (N.m-3) (CNEQ)
    to the internal volume forces (BSIG)
    Matrices
    matrix of shape (interpolation) functions
    matrix of derivatives of shape functions

## Slide 19: Imbalance
  Imbalance = measure of deviation of equilibrium
  The balance is obtained when
    norm of the imbalance vector, for instance infinity norm
    computational precision (given by user)
    reference force for the studied problem

## Slide 20: Non linear behavior
  Introduction of the linear elastic stiffness matrix
    with
  Equilibrium can be re written
    nodal displacements
    linear strains (« small » strains) (EPSI)
    complementary non linear stresses
    Hooke matrix (ELAS)
    elastic stiffness matrix (RIGI)

## Slide 21: Introducing the prescribed displacements
  Boundary condition matrix
    on
  Lagrange Multipliers
    For a lin. system without prescribed displacements:
    We add new unknowns
    with
    Equilibrium is now written:
    boundary condition matrix (BLOQ, RELA)
    prescribed nodal displacements (DEPI)
    Lagrange multipliers
depends on !!
non linear behavior,
large displacements,
following forces,
…

## Slide 22: Incremental decomposition (1/2)
  Computation on a time step between and
    known state beginning of time step
    unknown state end of time step
  Incremental decomposition of nodal displacements
    and
    and so
    estimation of displacement at iteration
    estimation of displacement increment at iteration
    correction of displacement increment at iteration
  Incremental decomposition of boundary conditions

## Slide 23: Incremental decomposition (2/2)
  Incremental decomposition of equilibrium
  Equilibrium is finally written

## Slide 24: Imbalance minimization algorithm
  Simple algorithm
    initializations
    reaction forces (REAC)
    convergence norm (MAXI 'ABS')
    first imbalance (residual) (BSIG)
    While:
    resolution (RESO)
    estim. displacements
    estim. strains (EPSI)
    estim. stresses (COMP)
    estim. reaction forces (REAC)
    new imbalance (residual) (BSIG)
    End

## Slide 25: UNPAS operation
Initializations, CHARMECA
1st imbalance evaluation
1st RESO and magnitude of convergence
RESO
Integration of the behavioral law CHARMECA
New imbalance evaluation
no
yes
Acquisition of options, materials updating, WTABLE, …
Stiffness matrix calculation , external prescribed forces
Displacement increment on the step
(RESO operator)
Convergence norm: measure the step, along and
correction of the displ. increment on the step (RESO operator)
displacement increment on the step (ZDEPT)
Magnitude of the imbalance < criterion (PRECISION, FTOL, MTOL) ??
Variation of the strains increment between 2 iterations < criterion ??
Results recording
Equilibrium reached?
Iteration engine, computes the imbalance between the internal and external forces (BSIG operator)
Non convergence detection:
  maximum number of iterations reached
  significant increase of the imbalance over several iterations
Forced convergence process
Convergence acceleration
Strains increment calculation on the step (EPSI operator)
Stresses , internal variables calculation, end of the step (COMP op.)
reaction forces (REAC operator)
new imbalance (BSIG operator)
« Non convergence » detected ?
no
yes
End
no
Convergence ?
Forced Convergence:
Restart from the out of unbalanced state
yes
Imbalance correction from the 3 previous imbalances (ACT3 operator)

## Slide 26: Users procedures in PASAPAS PERSO1 REEV_MEC CHARMECA PERSO2 REEV_THE CHARTHER PARATHER

## Slide 27: Users procedures: instructions for use
  There exists 7 users procedures called at different stages of PASAPAS algorithm
  PERSO1 PERSO2 REEV_MEC REEV_THE CHARMECA CHARTHER PARATHER
  1) According to the desired action, choose the procedure to be used as a function of its location on the algorithm
  for instance: since PERSO1 is called after computing a time step it is dedicated to update the next time step data e.g. boundary conditions, material parameters, …
  2) Analyze the procedure syntax - in the PASAPAS manual pages - In the PASAPAS, UNPAS or TRANSNON procedures
  the following table recalls the procedures syntaxes

## Slide 28: PERSO1 Procedure example
  3) Define the desired procedure
  DEBP PERSO1 T1*'TABLE' ;
  MESS 'Hello! The PERSO1 procedure is talking to you.' ;
  FINP ;
  4) Indicate in the PASAPAS table that this procedure should be called
  TAB1 . 'MODELE' = MOD1 ;
  TAB1 . 'CARACTERISTIQUES' = MAT1 ;
  TAB1 . 'TEMPS_CALCULES' = PROG 1. 2. 3. 4. ;
  TAB1 . 'PROCEDURE_PERSO1' = VRAI ;
  ...
  ...
  PASAPAS TAB1 ;

## Slide 29: Users procedures LIST
  With
  T1 : the PASAPAS table
  TPS1 : the current calculated time
  N1 : the call number of the procedure (0 or 1)  see the PASAPAS procedure
  T2 : the output table (only for the CHARMECA and CHARTHER procedures)
Name | Index to be activated in PASAPAS table | Syntax | Function
PERSO1 | TAB1 . 'PROCEDURE_PERSO1' = VRAI ; | PERSO1 T1 ; | Updates the problem after the mechanical calculation step
REEV_MEC | TAB1 . 'PROCEDURE_REEV_MEC' = VRAI ; | REEV_MEC T1 N1 ; | Ditto (but in BO_BOTH)  the step can be started again
CHARMECA | TAB1 . 'PROCEDURE_CHARMECA' = VRAI ; | T2 = CHARMECA T1 TPS1 ; | Mechanical loads addition during UNPAS iterations
PERSO2 | TAB1 . 'PROCEDURE_PERSO2' = VRAI ; | PERSO2 T1 ; | Updates the problem after the thermal calculation step
REEV_THE | TAB1 . 'PROCEDURE_REEV_THE' = VRAI ; | REEV_THE T1 N1 ; | Ditto (but in PASAPAS)  the step can be started again
CHARTHER | TAB1 . 'PROCEDURE_CHARTHER' = VRAI ; | T2 = CHARTHER T1 TPS1 ; | Thermal loads addition during TRANSNON iterations
PARATHER | TAB1 . 'PROCEDURE_PARATHER' = VRAI ; | PARATHER T1 TPS1 ; | Updating of the external variables of thermal parameters

## Slide 30: A few remarks
  Instructions inside these procedures are free !!!
  CHARMECA and CHARTHER output is a table with 2 possible indexes:
    - 'ADDI_MATRICE' contains the stiffness matrices (RIGIDITE type object) to be added to the 1st member
    - 'ADDI_SECOND' contains the CHPOINT to be added to the 2nd member (nodal forces)
  For large displacements ('GRANDS_DEPLACEMENTS' option), CHARMECA is called on the deformed shape

## Slide 31: A simple example
  Random variation of Young’s modulus map at each time step
OPTI 'DIME' 2 'ELEM' 'QUA4' ;
P0 = 0. 0. ; P1 = 1. 0. ;
L1 = DROI 1 P0 (0. 0.1) ;
S1 = L1 TRAN 10 (1. 0.) ;
L2 = S1 COTE 3 ; P2 = L2 POIN 'PROC' (1. 0.) ;
MO = MODE S1 'MECANIQUE' ;
MA = MATE MO 'YOUN' 200.E9 'NU' 0.3 ;
BL = (BLOQ 'UX' L1) ET (BLOQ 'UY' P0) ;
F = PRES 'MASS' MO L2 -1.E8 ;
EV = EVOL 'MANU' (PROG 0. 1.) (PROG 0. 1.) ;
CHA = CHAR 'MECA' F EV ;
TAB1 = TABL ;
TAB1 . 'MODELE' = MO ;
TAB1 . 'CARACTERISTIQUES' = MA ;
TAB1 . 'BLOCAGES_MECANIQUES' = BL ;
TAB1 . 'CHARGEMENT' = CHA ;
TAB1 . 'TEMPS_CALCULES' = PROG 0.1 'PAS' 0.1 1. ;
TAB1 . 'PROCEDURE_PERSO1' = VRAI ;
PASAPAS TAB1 ;
EVU = EVOL 'TEMP' TAB1 'DEPLACEMENTS' 'UX' P2 ;
DESS EVU ;
DEBP PERSO1 T1*'TABLE' ;
MOD = T1 . 'WTABLE' . 'MO_TOT' ;
MAIL = EXTR MOD 'MAIL' ;
CHPYO = BRUI 'BLAN' 'UNIF' 200.E9 150.E9 MAIL ;
CHMYO = CHAN 'CHAM' CHPYO MOD 'RIGIDITE' ;
MAT = MATE MOD 'YOUN' CHMYO 'NU' 0.3 ;
T1 . 'WTABLE' . 'CARACTERISTIQUES' = MAT ;
FINP ;

## Slide 32: Exercise 1: beam with following force Download the starting file on the website: http://www-cast3m.cea.fr/index.php?page=exemples&exemple=formation_pasapas_1_initial

## Slide 33: Exercise 1: beam with Following force
  Beam bending
  base is clamped
  point shear force at the top of the beam (perpendicular to the beam)
  large displacement at the top of the beam
  Problem: the force is calculated on the initial shape and not updated
  Purpose: to correctly apply the force during the calculation
  It’s up to you!
F
Deformed shape + reaction

## Slide 34: Exercise 1: beam with Following force
  A few indications …
  Useful objects
  P2 : point at the top of the beam, where the force is prescribed
  EV1 : force magnitude to be applied as a function of time
  Useful operators
  EXTR, COS, SIN
  IPOL : to interpolate the force magnitude as a function of the calculated step
  FORC : to apply a point force

## Slide 35: Exercise 1: beam with Following force
  Solution
  - use option 'GRANDS_DEPLACEMENTS' (equilibrium verified on the deformed shape)
  use procedure PERSO1 (1 call / time step) to re-calculate the force on deformed shape (at beginning of time step)
  create a “load” with it (CHARGEMEnt type object)
  overwrite the load in WTABLE
PERSO1 procedure Main program
  TAB1 . 'GRANDS_DEPLACEMENTS' = VRAI ;
  TAB1 . 'PREDICTEUR' = 'HPP' ;
  TAB1 . 'PROCEDURE_PERSO1' = VRAI ;
  TAB1 . 'MY_DATA' = TABL ;
  TAB1 . 'MY_DATA' . 'EVOL' = EV1 ;
  TAB1 . 'MY_DATA' . 'POINT' = P2 ;
  DEBP PERSO1 T1*'TABLE' ;
  * donnees utiles
  TAM = T1 . 'MY_DATA' ;
  PF = TAM . 'POINT' ;
  EV = TAM . 'EVOL' ;
  * angle de rotation de la section droite
  U1 = T1 . 'ESTIMATION' . 'DEPLACEMENTS' ;
  RS = EXTR U1 'RZ' PF ;
  RSD = RS * 180. / PI ;
  * direction de l'effort
  DIR1 = (COS RSD) (SIN RSD) ;
  * creation du second membre
  F1 = FORC DIR1 PF ;
  CHAR2 = CHAR 'MECA' F1 EV ;
  T1 . 'WTABLE' . 'CHARGEMENT' = CHAR2 ;
  FINP ;

## Slide 36: Exercise 1: beam with Following force
  Results
Deformed shape + reaction
Displacements Ux and Uy as a function of time

## Slide 37: Exercise 1: beam with Following force
  Solution (bis)
  idem but with the CHARMECA procedure
  suppress initial mechanical loading
  no need of CHARGEMEnt type object
  longer: 1 call / each iteration / time step
  results are identical
CHARMECA procedure Main program
  DEBP CHARMECA T1*'TABLE' TPS1*'FLOTTANT' ;
  * donnees utiles
  TAM = T1 . 'MY_DATA' ;
  PF = TAM . 'POINT' ;
  EV = TAM . 'EVOL' ;
  * angle de rotation de la section droite
  U1 = T1 . 'ESTIMATION' . 'DEPLACEMENTS' ;
  RS = EXTR U1 'RZ' PF ;
  RSD = RS * 180. / PI ;
  * direction de l'effort
  DIR1 = (COS RSD) (SIN RSD) ;
  * creation du second membre
  VAL1 = IPOL TPS1 EV ;
  F1 = FORC (VAL1 * DIR1) PF ;
  T2 = TABLE ;
  T2 . 'ADDI_SECOND' = F1 ;
  FINP T2 ;
  ***TAB1 . 'CHARGEMENT' = CHAR1 ;
  TAB1 . 'GRANDS_DEPLACEMENTS' = VRAI ;
  TAB1 . 'PREDICTEUR' = 'HPP' ;
  TAB1 . 'PROCEDURE_CHARMECA' = VRAI ;
  TAB1 . 'MY_DATA' = TABL ;
  TAB1 . 'MY_DATA' . 'EVOL' = EV1 ;
  TAB1 . 'MY_DATA' . 'POINT' = P2 ;

## Slide 38: Exercise 1: beam with Following force
  Solution (ter)
  idem, but the force is updated on the deformed shape at the end of time step!
  more precise: when converged, the deformed geometry is exactly perpendicular to applied force
  - watch out: can become unstable !
CHARMECA procedure Main program
  DEBP CHARMECA T1*'TABLE' TPS1*'FLOTTANT' ;
  * donnees utiles
  TAM = T1 . 'MY_DATA' ;
  PF = TAM . 'POINT' ;
  EV = TAM . 'EVOL' ;
  * angle de rotation de la section droite
  DRS = 0. ;
  SI (EGA (TYPE ZDEPT) 'CHPOINT') ;
  DRS = EXTR ZDEPT 'RZ' PF ;
  FINSI ;
  U0 = T1 . 'CONTINUATION' . 'DEPLACEMENTS' ;
  RS = (EXTR U0 'RZ' PF) + DRS ;
  RSD = RS * 180. / PI ;
  * direction de l'effort
  DIR1 = (COS RSD) (SIN RSD) ;
  * creation du second membre
  VAL1 = IPOL TPS1 EV ;
  F1 = FORC (VAL1 * DIR1) PF ;
  T2 = TABLE ;
  T2 . 'ADDI_SECOND' = F1 ;
  FINP T2 ;
  ***TAB1 . 'CHARGEMENT' = CHAR1 ;
  TAB1 . 'GRANDS_DEPLACEMENTS' = VRAI ;
  TAB1 . 'PREDICTEUR' = 'HPP' ;
  TAB1 . 'PROCEDURE_CHARMECA' = VRAI ;
  TAB1 . 'MY_DATA' = TABL ;
  TAB1 . 'MY_DATA' . 'EVOL' = EV1 ;
  TAB1 . 'MY_DATA' . 'POINT' = P2 ;

## Slide 39: Exercise 2: rupture by elements removal Download the starting file on the website: http://www-cast3m.cea.fr/index.php?page=exemples&exemple=formation_PASAPAS_2_INITIAL

## Slide 40: Exercise 2: rupture by elements removal
  Traction of a perforated plate
    elastic behavior, large displacements
  Purpose: to model fracture by removing elements during calculations We will use a simple criterion based on the 1st principal stress:
  fracture if sI ≥ 22 GPa
  It’s up to you!
Boundary conditions
sI stress and
reaction forces
on the deformed shape
Imposed
displacement

## Slide 41: Exercise 2: rupture by elements removal
  A few indications …
  Useful objects
  PRIN: principal stress field calculations
  CHAN: change the support points of a field by elements
  ELEM: select the elements of a field that meets a criteria
  REDU: reduction of a model on a sub-mesh
  Useful information
  Modify the temporary objects for computation in TAB1 . WTABLE

## Slide 42: Exercise 2: rupture by elements removal
  Solution
  - reduce time steps
  - use the PERSO1 procedure
  extract the model and the calculated stresses (T1 . ESTIMATION)
  calculate the principal stresses
  determine the mesh of “intact elements”
  - reduce the model on this mesh
  - overwrite the model in the working table WTABLE
PERSO1 procedure Main program
  TAB1 . 'PROCEDURE_PERSO1' = VRAI ;
  TAB1 . 'TEMPS_CALCULES' = PROG 0.1 'PAS' 0.1 0.6
  'PAS' 0.01 1. ;
  DEBP PERSO1 T1*'TABLE' ;
  MO1 = T1 . 'WTABLE' . 'MODELE' ;
  SG1 = T1 . 'ESTIMATION' . 'CONTRAINTES' ;
  SGP1 = PRIN SG1 MO1 ;
  SG11 = CHAN 'GRAVITE' (EXCO 'SI11' SGP1) MO1 ;
  MAIL2 = SG11 ELEM 'INFERIEUR' 2.2E10 ;
  MO2 = REDU MO1 MAIL2 ;
  T1 . 'WTABLE' . 'MODELE' = MO2 ;
  FINP ;

## Slide 43: Exercise 2: rupture by elements removal
  Results
Strength / displacement curve
Undependable model:
results quite sensitive to time/space discretization

## Slide 44: Exercise 2: rupture by elements removal
  Solution (bis)
  - reduce time steps
  - use the PERSO1 procedure
  extract the model and the calculated stresses (T1 . ESTIMATION)
  calculate the principal stresses
  determine the mesh of intact elements
  - reduce the boundary conditions on this mesh
  - overwrite the boundary conditions in the working table WTABLE
  DEBP PERSO1 T1*'TABLE' ;
  MO1 = T1 . 'WTABLE' . 'MODELE' ;
  MAIL1 = EXTR MO1 'MAIL' ;
  SG1 = T1 . 'ESTIMATION' . 'CONTRAINTES' ;
  SGP1 = PRIN SG1 MO1 ;
  SG11 = CHAN 'GRAVITE' (EXCO 'SI11' SGP1) MO1 ;
  MAIL2 = SG11 ELEM 'INFERIEUR' 2.2E10 ;
  MAIL3 = DIFF MAIL1 MAIL2 ;
  NE3 = NBEL MAIL3 ;
  SI (NE3 > 0) ;
  MESS ' [PERSO1 :] Removal of' NE3 'elements' ;
  BL01 = T1 . 'WTABLE' . 'BLOCAGES_MECANIQUES' ;
  MAILBL1 = EXTR BL01 'MAIL' ;
  MAILBL2 = MAILBL1 ELEM 'APPU' 'LARG' MAIL3 ;
  MAILBL3 = DIFF MAILBL1 MAILBL2 ;
  BL02 = REDU BL01 MAILBL3 ;
  T1 . 'WTABLE' . 'BLOCAGES_MECANIQUES' = BL02 ;
  FINSI ;
  FINP ;
PERSO1 procedure Main program
  TAB1 . 'PROCEDURE_PERSO1' = VRAI ;
  TAB1 . 'TEMPS_CALCULES' = PROG 0.1 'PAS' 0.1 0.6
  'PAS' 0.01 1. ;

## Slide 45: Exercise 2: rupture by elements removal
  Results
Strength / displacement curve
Undependable model:
results quite sensitive to time/space discretization

## Slide 46: TRANSNON operation thermal solver

## Slide 47: Reminder on equations
  Local equations in transient thermal analysis
    heat flux density on
    heat equation on
    prescribed flux on
    prescribed temperature on

## Slide 48: Reminder on equations
  Weak form + FE discretization
    Vectors of Equivalent Nodal Heat (W)
    to the prescribed surface heat flux (J.m-2) (FLUX)
    to the prescribed convection flux (J.m-2) (CONV)
    to the prescribed radiation flux (J.m-2)
    to the prescribed volume heat (J.m-3) (SOUR)
    Matrices
    capacity matrix (J.K-1) (CAPA)
    conductivity matrix (W.K-1) (COND)
    matrix of shape (interpolation) functions
    matrix of derivatives of shape functions

## Slide 49: Theta method
  Weak form + FE discretization
  Time discretization: theta method
    with:
    time step
    vector of nodal temperatures at time
    vector of nodal temperatures at time
    and are estimated:
    at time
    at temperature
    relaxation coefficient (between 0 and 1)
    explicit scheme
    implicit scheme (default value)

## Slide 50: TRANSNON operation
Initializations, CHARTHER
State of system at
PARATHER
Material updating
Matrix calculation and
CHARTHER
Calculation of
RESO
PERSO2
Results recording and exit
Convergence ?
End of time steps?
no
i = i + 1
no
yes
yes
Options, times calculated, units (°C or K), initial state, shape functions (for radiation)…
External variables updating, material characteristics Calculation of conductivity matrix (cond. + conv. + radi. + constrain.)
and capacity matrix at temperature and time
Calculation of 2nd member (T impo. + T conv. + T rayo. + Flux impo.) at temperature and time
We define the operator as:
Temperature increment calculation:
and so we get:
and also:
Measure the maximal difference on the temperature increment for two successive steps:
Crit = [MAXI 'ABS' ] / [MAXI 'ABS' ]
User procedure
State of system at
PARATHER
Material updating
CHARTHER
Calculation of
Next step Initialization
Remark: when TRANSNON is called by PASAPAS,
the time step loop is performed once
Convergence acceleration
Criterion
If the criterion is small enough:
Crit ≤ 'PRECISION' (1.E-4 by default)

## Slide 51: Exercise 3: heat source depending on temperature Download the starting file on the website: http://www-cast3m.cea.fr/index.php?page=exemples&exemple=formation_pasapas_3_initial

## Slide 52: Exercise 3: heat generation depending on temperature
  Square section with heat source and cooled by convection
  Purpose: make the problem depending on parameters
     Conductivity as a function of temperature
     Convection as a function of time
     Source as a function of temperature
  It’s up to you!
Heat source
Convection
Convection
h [W.m-2.K-1]
t [s]
10
200
0
105

## Slide 53: Exercise 3: heat generation depending on temperature
  A few indications …
  Useful objects
  MAIL1 : source mesh
  MOD1 : thermal model reduced on MAIL1
  Useful operators
  REDU : to reduce the temperature field on the "source“ area
  SOUR : to impose a volumetric heat source

## Slide 54: Exercise 3: heat generation depending on temperature
  Solution
  use the PERSO2 procedure (called at each time step)
  recalculate the source (2nd member) as a function of temperatures at the beginning of the time step
  create a “load” with it and overwrite the load in WTABLE
PERSO2 procedure Main program
DEBP PERSO2 T1*'TABLE' ;
MA1 = T1 . 'AMOI' . 'MAIL' ;
MO1 = T1 . 'AMOI' . 'MODE' ;
* reduction du champ de temperatures au maillage de la source
CHT1 = T1 . 'ESTIMATION' . 'TEMPERATURES' ;
CHT2 = REDU CHT1 MA1 ;
* calcul du champ de source a partir du champ de temperature
CHS = 4.E6 * (EXP (-1. * (((CHT2 - 1000.) / 700.) ** 2))) ;
* creation du second membre et d'un chargement
CHFL1 = SOUR MO1 CHS ;
EV1 = EVOL 'MANU' (PROG 0. TPSMAX) (PROG 1. 1.) ;
CHA1 = CHAR 'Q' CHFL1 EV1 ;
* modification du chargement dans la table de calcul
T1 . 'WTABLE' . 'CHARGEMENT' = CHA1 ;
FINP T2 ;
  LT = PROG -1.E6 1.E6 ;
  LL = 200. + (0.3 * LT) ;
  LAMBDA = EVOL 'MANU' 'T' LT 'K' LL ;
  HCONV = EVOL 'MANU' 'TEMP' (PROG 0. TPSMAX) 'H' (PROG 10. 200.) ;
  VSOUR = 4.E6 * (EXP (-1. * (((T_INI - 1000.) / 700.) ** 2))) ;
  TAB1 . 'PROCEDURE_PERSO2' = VRAI ;
  TAB1 . 'MY_DATA' = TABL ;
  TAB1 . 'MY_DATA' . 'MAIL' = MAIL1 ;
  TAB1 . 'MY_DATA' . 'MODE' = MOD1 ;

## Slide 55: Exercise 3: heat generation depending on temperature
  Solution (bis)
  - suppress loading CHA1 (heat source)
  use the CHARTHER procedure (called at each step iteration)
  recalculate the source (2nd member) as a function of temperatures at the beginning of the time step
CHARTHER procedure Main program
DEBP CHARTHER T1*'TABLE' TPS1*'FLOTTANT' ;
MA1 = T1 . 'MY_DATA' . 'MAIL' ;
MO1 = T1 . 'MY_DATA' . 'MODE' ;
* reduction du champ de temperatures au maillage de la source
CHT1 = T1 . 'ESTIMATION' . 'TEMPERATURES' ;
CHT2 = REDU CHT1 MA1 ;
* calcul du champ de source a partir du champ de temperature
CHS = 4.E6 * (EXP (-1. * (((CHT2 - 1000.) / 700.) ** 2))) ;
* creation du second membre
CHFL1 = SOUR MO1 CHS ;
* sortie du second membre
T2 = TABL ;
T2 . 'ADDI_SECOND' = CHFL1 ;
FINP T2 ;
  LT = PROG -1.E6 1.E6 ;
  LL = 200. + (0.3 * LT) ;
  LAMBDA = EVOL 'MANU' 'T' LT 'K' LL ;
  HCONV = EVOL 'MANU' 'TEMP' (PROG 0. TPSMAX) 'H' (PROG 10. 200.) ;
  ***TAB1 . 'CHARGEMENT' = CHA2 ;
  TAB1 . 'PROCEDURE_CHARTHER' = VRAI ;
  TAB1 . 'MY_DATA' = TABL ;
  TAB1 . 'MY_DATA' . 'MAIL' = MAIL1 ;
  TAB1 . 'MY_DATA' . 'MODE' = MOD1 ;

## Slide 56: Exercise 3: heat generation depending on temperature
  Solution (ter)
  idem
  use the CHARTHER procedure (called at each step iteration)
  recalculate the source (2nd member) as a function of temperatures at previous iteration (i.e. at the end of the time step)
CHARTHER procedure Main program
DEBP CHARTHER T1*'TABLE' TPS1*'FLOTTANT' ;
MA1 = T1 . 'MY_DATA' . 'MAIL' ;
MO1 = T1 . 'MY_DATA' . 'MODE' ;
* reduction du champ de temperatures au maillage de la source
CHT1 = T1 . 'WTABLE' . 'THER_COURANT' ;
CHT2 = REDU CHT1 MA1 ;
* calcul du champ de source a partir du champ de temperature
CHS = 4.E6 * (EXP (-1. * (((CHT2 - 1000.) / 700.) ** 2))) ;
* creation du second membre
CHFL1 = SOUR MO1 CHS ;
* sortie du second membre
T2 = TABL ;
T2 . 'ADDI_SECOND' = CHFL1 ;
FINP T2 ;
  LT = PROG -1.E6 1.E6 ;
  LL = 200. + (0.3 * LT) ;
  LAMBDA = EVOL 'MANU' 'T' LT 'K' LL ;
  HCONV = EVOL 'MANU' 'TEMP' (PROG 0. TPSMAX) 'H' (PROG 10. 200.) ;
  ***TAB1 . 'CHARGEMENT' = CHA1 ;
  TAB1 . 'PROCEDURE_CHARTHER' = VRAI ;
  TAB1 . 'MY_DATA' = TABL ;
  TAB1 . 'MY_DATA' . 'MAIL' = MAIL1 ;
  TAB1 . 'MY_DATA' . 'MODE' = MOD1 ;

## Slide 57: Exercise 3: heat generation depending on temperature
  Results
PERSO2 or CHARTHER (beginning time step)
CHARTHER (end of time step)

## Slide 58: Exercise 4: thermo-mechanical gap closing Download the starting file on the website: http://www-cast3m.cea.fr/index.php?page=exemples&exemple=formation_pasapas_4_initial

## Slide 59: Exercise 4: thermo-mechanical gap closing
  Two bars expand and get in contact
  thermal expansion
  unilateral mechanical contact
  Purpose: add thermal contact, this is to say the heat transfer when the mechanical contact takes place.
  It’s up to you!
gap
bar 1
bar 2

## Slide 60: Exercise 4: thermo-mechanical gap closing
  A few indications …
  Useful objects
  P2 et P3: points on the left/right of the gap
  L2 et L3: lines on the left/right of the gap
  Useful operators
  COOR: points coordinates
  RELA: relation between degrees of freedom
  Modify thermal boundary conditions of WTABLE

## Slide 61: Exercise 4: thermo-mechanical gap closing
  Solution
  check the mechanical + thermal convergence
  create a new constraint: relation between the temperatures T on line L2 = T on line L3 with RELA operator
  use REEV_MEC to modify the thermal boundary conditions
  calculate the gap at iteration time
  modify thermal boundary conditions in WTABLE as a function of the gap
REEV_MEC Procedure Main program
  DEBP REEV_MEC T1*'TABLE' N1*'ENTIER' ;
  U1 = T1 . 'ESTIMATION' . 'DEPLACEMENTS' ;
  WT = T1 . 'WTABLE' ;
  TAM = T1 . 'MY_DATA' ;
  * calcul du jeu
  PT2 = TAM . 'POINT_2' ;
  PT3 = TAM . 'POINT_3' ;
  X2 = (COOR 1 PT2) + (EXTR U1 'UX' PT2) ;
  X3 = (COOR 1 PT3) + (EXTR U1 'UX' PT3) ;
  J1 = X3 - X2 ;
  * si jeu ferme, on utilise le blocage thermique initial + le RELA
  SI (J1 <EG 1.E-15) ;
  WT . 'BLOCAGES_THERMIQUES' = (TAM . 'BLOQ_0') ET
  (TAM . 'BLOQ_1') ;
  * si jeu ouvert, on utilise le blocage thermique initial seul
  SINON ;
  WT . 'BLOCAGES_THERMIQUES' = TAM . 'BLOQ_0' ;
  FINSI ;
  FINP ;
  TAB1 . 'CONVERGENCE_MEC_THE' = VRAI ;
  TAB1 . 'PROCEDURE_REEV_MEC' = VRAI ;
  TAB1 . 'MY_DATA' = TABL ;
  TAB1 . 'MY_DATA' . 'POINT_2' = P2 ;
  TAB1 . 'MY_DATA' . 'POINT_3' = P3 ;
  TAB1 . 'MY_DATA' . 'BLOQ_0' = CL_TH ;
  TAB1 . 'MY_DATA' . 'BLOQ_1' = RELA 'T' L2 - 'T' L3 ;

## Slide 62: Exercise 4: thermo-mechanical gap closing
  Results
During contact: "perfect" conduction
Without contact: bars are insulated

## Slide 63: Exercise 4: thermo-mechanical gap closing
  Results
  Changes made in REEV_MEC are taken into account at the same time step (due to thermo-mechanics convergence loop BO_BOTH)
  It will be different with PERSO1. Changes are taken into account at the next time step
Temperatures as a function of time on the left side and on the riht side of the gap
Gap distance as a function of time

## Slide 64: Exercise 4: thermo-mechanical gap closing
  Solution (bis)
  convective heat transfer in a transition element
  use of an heat transfer coefficient depending on pressure
  pressure is described through a loading named 'PC'
  updating of the loading 'PC' in REEV_MEC
REEV_MEC procedure Main program
  ** Modele de convection variable entre les barreaux
  MRACC = RACC (1.1 * JEU_INI) L2 L3 ;
  MODRACC = MODE MRACC 'THERMIQUE' 'CONVECTION' ;
  HVSP = EVOL 'MANU' 'PC' (PROG 0. 5.E8 5.1E8)
  'H' (PROG 0. 1.E4 1.E4) ;
  MATRACC = MATE MODRACC 'H' HVSP ;
  MOD_TH = MODT1 ET MODT2 ET MODRACC ;
  MAT_TH = MATT1 ET MATT2 ET MATRACC ;
  ** Chargement initial decrivant la pression de contact
  CH_PC = MANU 'CHPO' MRACC 'PC' 0. ;
  CHA2 = CHAR 'PC' CH_PC EV1 ;
  TAB1 . 'CHARGEMENT' = CHA1 ET CHA2 ;
  TAB1 . 'CONVERGENCE_MEC_THE' = VRAI ;
  TAB1 . 'PROCEDURE_REEV_MEC' = VRAI ;
  TAB1 . 'MY_DATA' = TABL ;
  TAB1 . 'MY_DATA' . 'LIGNE_3' = L3 ;
  TAB1 . 'MY_DATA' . 'MAIL' = MRACC ;
  TAB1 . 'MY_DATA' . 'EVOL' = EV1 ;
  TAB1 . 'MY_DATA' . 'CHAR_0' = CHA1 ;
  DEBP REEV_MEC T1*'TABLE' N1*'ENTIER' ;
  R1 = T1 . 'ESTIMATION' . 'REACTIONS' ;
  WT = T1 . 'WTABLE' ;
  TAM = T1 . 'MY_DATA' ;
  L3 = TAM . 'LIGNE_3' ;
  MR = TAM . 'MAIL' ;
  SI ((T1 . 'ESTIMATION' . 'TEMPS') NEG 0.) ;
  * calcul de la pression de contact
  PARA_P = (MAXI 'ABS' (RESU (REDU R1 L3))) / (MESU L3) ;
  * chargment decrivant le parametre 'PC'
  CH_PC = MANU 'CHPO' MR 'PC' PARA_P ;
  EV1 = TAM . 'EVOL' ;
  CHA3 = CHAR 'PC' CH_PC EV1 ;
  * on ecrase le chargement global de WTABLE
  WT . 'CHARGEMENT' = (TAM . 'CHAR_0') ET CHA3 ;
  FINS ;
  FINP ;

## Slide 65: Exercise 4: thermo-mechanical gap closing
  Results (bis)
  The heat transfer is made with different temperatures over the gap
  The temperature evolution is smoother
Temperatures as a function of time on the left side and on the riht side of the gap
Gap distance as a function of time

## Slide 66: Annexes

## Slide 67: Annex: algorithmic control parameters
  General
    NB_BOTH (ENTIER) Maximum number of iterations for the thermo-mechanical
    convergence loop
    MAXITERATION (ENTIER) Maximum number of iterations (49)
  Mechanics
    PRECISION (FLOTTANT) Criterion to compare the imbalance (1.E-4)
    FTOL (FLOTTANT) Tolerance for strength equilibrium
    MTOL (FLOTTANT) Tolerance for moments equilibrium
    GRANDS_DEPLACEMENTS (LOGIQUE) Reference configuration = deformed configuration
    PREDICTEUR = 'HPP' Small displacements hypothesis  1st convergence
    then use the
    large displacements hypothesis  2nd convergence PRECISINTER (FLOTTANT) Precision for the constitutive laws integration local
    problem (1.E-8)
    CONVERGENCE_FORCEE (LOGIQUE) Forced convergence use or not in case of non convergence (VRAI)
    MAXSOUSPAS (ENTIER) Max. number of sub-steps during forced convergence (200)
    DELTAITER (ENTIER) Number of steps over which non convergence is tested

## Slide 68: Annex: algorithmic control parameters
  Thermal
    PROCEDURE_THERMIQUE (MOT) Procedures to call:
    - NONLINEAR TRANSNON procedure - LINEAR TRANSLIN procedure
    - DUPONT DUPONT2 procedure
    RELAXATION_THETA (FLOTTANT) Relaxation coefficient for the q-method (1)
  Thermo-mechanical coupling
    CONVERGENCE_MEC_THE (LOGIQUE) Indicates that the thermo-mechanical loop should be repeated in case of dependence (FAUX)
    CRITERE_COHERENCE (FLOTTANT) Precision for the thermo-mechanical convergence, tested on thermal results (1.E-2)
    PROJECTION (LOGIQUE) Indicates that the thermal and mechanical meshes are different while the problem is coupled (FAUX)

## Slide 69: Annex: imbalance minimization in Gibiane
  Simplified UNPAS algorithm (see the @SOLVMEC procedure)
    [small displacements / strains]
    fex1 = TIRE char tps1 ‘MECA’ ;
    flx1 = TIRE char tps1 ‘DIMP’ ;
    resi0 = fex1 + fr0 – fi0 + flx1 – flx0 ;
    fref = MAXI ‘ABS’ (fex1 + fr0) ;
    k = (RIGI mod mat) ET blo ;
    REPE b1 100 ;
    ddu = RESO k resi0 ;
    u1 = u0 + ddu ;
    fr1 = REAC blo u1 ;
    eps1 = EPSI mod u1 ;
    sig1 = ... COMP eps0 eps1 ...
    fi1 = BSIG mod sig1 ;
    resi1 = fex1 + fr1 – fi1 ;
    crit1 = (MAXI ‘ABS’ resi1) / fref ;
    SI (crit1 < precis) ;
    QUIT b1 ;
    FINSI ;
    u0 = u1 ;
    resi0 = resi1 ;
    FIN b1 ;

## Slide 70: Annex: imbalance minimization in Gibiane
  Simplified UNPAS algorithm (see the @SOLVMEC procedure)
    [large displacements, updated lagrangian]
    fex1 = TIRE char tps1 ‘MECA’ ;
    flx1 = TIRE char tps1 ‘DIMP’ ;
    resi0 = fex1 + fr0 – fi0 + flx1 – flx0 ;
    fref = MAXI ‘ABS’ (fex1 + fr0) ;
    conf0 = FORM u0 ;
    u00 = u0 ; moving to the current configuration (beginning of time step)
    k = (RIGI mod mat) ET blo ET (KSIG mod sig0) ;
    REPE b1 100 ;
    ddu = RESO k resi0 ;
    u1 = u0 + ddu ;
    fr1 = REAC blo u1 ;
    du = u1 – u00 ;
    deps = EPSI mod du ; strain increment
    eps1 = eps0 + deps ;
    sig1 = ... (COMP eps0 eps1, EXCO, ...)
    sig1 = PICA mod sig1 du ; moving stresses to the final configuration
    FORM u1 ;
    fi1 = BSIG mod sig1 ; integration on the final configuration
    FORM conf0 ;
    resi1 = fex1 + fr1 – fi1 ;
    crit1 = (MAXI ‘ABS’ resi1) / fref ;
    SI (crit1 < precis) ;
    QUIT b1 ;
    FINSI ;
    u0 = u1 ;
    resi0 = resi1 ;
    FIN b1 ;

## Slide 71: Annex: convergence criteria (UNPAS)
  Convergence norms (after 1st RESO)
  Unbalance measure (at each UNPAS iteration)

## Slide 72: Annex: convergence criteria (UNPAS)
  Measure of strain increment variation between 2 iterations
  Convergence is reached if
    < PRECISION
    < PRECISION
    < PRECISION

## Slide 73: Annex: forced convergence to be finished…
  If non convergence is confirmed, the step is re-calculated:
  state at the beginning of the step is redefined
  the last “out of equilibrium“ state with minimal imbalance is chosen
  at the beginning of time step, are overwritten:
      the instant
      the material properties
      the displacements
      the internal variables
      the inelastic strains
      the stresses
  UNPAS is re-started with a time-step equal to zero
  no load increment, only disequilibrium
  allows to find a solution with the right behavior and equilibrium but with a different loading path

## Slide 74: DES/DANS DM2S SEMT
François DI PAOLA
Commissariat à l'énergie atomique et aux énergies alternatives
Centre de Saclay | 91191 Gif-sur-Yvette Cedex
  Etablissement public à caractère industriel et commercial | R.C.S Paris B 775 685 019